## Slide 1
4-BIT RISC CPU
Architecture • Datapath • Schematic • Testbench
A Verilog HDL project with a 3-stage pipeline
Focus: how the CPU fetches, decodes, executes, and verifies instructions
IF
ID
EX
MEM
WB
Project presentation • Functional simulation and current test results

## Slide 2
ALU VS CPU: WHAT IS THE DIFFERENCE?
26
ALU — Arithmetic Logic Unit
• A processing block inside the CPU
• Performs arithmetic: ADD, SUB
• Performs logic: AND, OR, XOR, NOT
• Produces a result and status flags (Zero, Carry)
• Does not fetch or decode instructions by itself
In this project: the ALU is 4-bit wide.
CPU — Central Processing Unit
• The complete processor system
• Fetches instructions using the PC and Instruction Memory
• Decodes instructions in the Control Unit
• Uses the Register File, ALU, MUXes and memory
• Updates the PC, flags and registers as instructions run
In this project: a 4-bit RISC CPU with a 3-stage pipeline.
Key idea: The ALU is one part of the CPU. The CPU controls the full instruction flow.

## Slide 3
HOW THE ALU WORKS INSIDE THE CPU
27
1. FETCH
PC + Instruction Memory
get the instruction
2. DECODE
Control Unit identifies
opcode and operands
3. EXECUTE
MUX selects inputs;
ALU computes result
4. MEMORY
Data Memory is used
when required
5. WRITE-BACK
MUX selects data;
register is updated
Example: ADD R1, R2
The CPU fetches and decodes the ADD instruction.
The ALU adds the values in R1 and R2.
The CPU writes the result back to the destination register.
Why the CPU needs more than an ALU
The ALU cannot choose the next instruction, read the instruction memory, or manage register write-back alone.
The CPU’s control and datapath blocks coordinate these actions.
ALU = calculation unit | CPU = complete instruction-processing system

## Slide 4
PRESENTATION ROADMAP
INTRODUCTION
02
01
CPU overview
02
Instruction format & registers
03
Main hardware blocks
04
Datapath schematic
05
Pipeline operation
06
Testbench & results
The presentation follows the same path as the data inside the CPU: instruction in → control → result out.

## Slide 5
WHAT IS A 4-BIT RISC CPU?
INTRODUCTION
03
• 4-bit datapath: the ALU and general-purpose registers process 4-bit values.
• RISC means a small, simple instruction set with a regular instruction format.
• The project is written in Verilog HDL and tested with Vivado/XSim.
• The design uses a 3-stage pipeline: IF, ID, and EX.
• The instruction word is 12 bits wide; the program counter is 4 bits wide.
12-bit instruction
4-bit data / ALU result
4 general-purpose registers
3 pipeline stages

## Slide 6
KEY DESIGN SPECIFICATIONS
INTRODUCTION
04
Datapath
4 bits
Data and ALU result width
Instruction
12 bits
Opcode + register fields + immediate/address
Program Counter
4 bits
Addresses 16 instruction locations
Instruction Memory
16 × 12
16 words, each 12 bits
Data Memory
16 × 4
16 words, each 4 bits
Register File
R0–R3
Four 4-bit registers
Pipeline
3 stages
IF → ID → EX
Note: these are the design dimensions described by the project; actual behavior must be confirmed by simulation.

## Slide 7
INSTRUCTION SET: 12-BIT FORMAT
INSTRUCTION SET
05
Instruction fields are fixed-width, so the decoder reads the same bit positions each time.
opcode
[11:8]
4 bit
Rd
[7:6]
2 bit
Rs
[5:4]
2 bit
imm / addr
[3:0]
4 bit
Register codes
R0 = 00 R1 = 01 R2 = 10 R3 = 11
Instruction
Opcode
Rd
Rs
imm/addr
Hex
ADD R1, R2
0000
01
10
0000
0x060
LDI R3, 10
0110
11
00
1010
0x6CA
JZ 9
1011
00
00
1001
0xB09
Example encodings are shown as documented in the project presentation material.

## Slide 8
INSTRUCTION FAMILIES AND DECODING
INSTRUCTION SET
06
• R-type: uses register operands, for example ADD R1, R2.
• I-type: uses an immediate value, for example LDI R3, 10.
• J-type: uses an address for control flow, for example JZ 9.
• The opcode tells the Control Unit which operation and control signals to select.
• The remaining fields identify destination/source registers or an immediate/address.
12-bit instruction
Opcode decoder
ALU / data
control
Jump / branch
control
Decoder outputs include ALU control, register write enable, memory write enable, and branch/jump indicators.

## Slide 9
BLOCK 1: PROGRAM COUNTER AND INSTRUCTION MEMORY
CPU COMPONENTS
07
Program
Counter (PC)
PC + 1
PC MUX
Instruction
Memory
12-bit instruction word
• PC holds the address of the instruction to fetch.
• PC + 1 calculates the next sequential address.
• PC MUX selects PC+1 or a jump target, depending on pc_sel.
• Instruction Memory stores 16 instructions, each 12 bits wide.

## Slide 10
BLOCK 2: INSTRUCTION REGISTER AND PIPELINE REGISTERS
CPU COMPONENTS
08
Instruction
Memory
IF/ID Register
(IR)
Control Unit
ID/EX Pipeline
Register
• IF/ID captures the fetched instruction so the next stage can decode it.
• The decoder reads the opcode and creates control signals.
• ID/EX stores instruction fields and control signals for execution.
• Pipeline registers keep stage-to-stage values stable between clock edges.
• When a jump is taken, the design uses flush control to clear younger instructions.

## Slide 11
BLOCK 3: CONTROL UNIT
CPU COMPONENTS
09
Opcode + fields
Instruction Decoder
ALU control: alu_ctrl
Operand select: alu_src_sel
Write-back: wb_sel / reg_we
Branch Unit
pc_sel / flush
The Control Unit does not calculate the data result. It tells the datapath which operation to perform and where the result should go.

## Slide 12
BLOCK 4: REGISTER FILE (R0–R3)
CPU COMPONENTS
10
R0
00
R1
01
R2
10
R3
11
Two read ports
qa and qb
One write-back path
wd → destination Rd
• The register file stores temporary 4-bit values used by instructions.
• Rd identifies the destination register; Rs identifies a source register.
• Write-back updates a register when reg_we is enabled.

## Slide 13
BLOCK 5: ARITHMETIC LOGIC UNIT (ALU)
CPU COMPONENTS
11
Operand A
(qa)
Operand B
(qb or imm)
4-bit ALU
Result [3:0]
Zero / Carry flags
• The ALU performs arithmetic and logic operations selected by alu_ctrl.
• The ALU result may be written to a register or used as a data-memory address.
• Zero indicates that the result is zero; Carry reports a carry/borrow-related condition for arithmetic.

## Slide 14
BLOCK 6: MULTIPLEXERS AND FLAGS
CPU COMPONENTS
12
PC MUX
PC+1 or jump target
Operand MUX
register operand or immediate
WB MUX
ALU result or memory data
Zero flag (Z)
Result equals 0
Carry flag (C)
Arithmetic carry status
A MUX selects one of several inputs. A flag register stores status information so later control logic, such as a conditional jump, can use it.

## Slide 15
BLOCK 7: DATA MEMORY AND WRITE-BACK
CPU COMPONENTS
13
ALU result
(address)
Data Memory
16 × 4 bits
Read data
WB MUX
Register file Rd
mem_we enables a memory write. wb_sel chooses the value sent back to Rd. For a load-like operation, memory data is selected; for an ALU operation, the ALU result is selected.

## Slide 16
CPU SCHEMATIC: FULL DATAPATH
SCHEMATIC
14
STAGE 1: IF
STAGE 2: ID
STAGE 3: EX / MEMORY / WB
PC
Instr.
Memory
IF/ID IR
Decoder
ID/EX Reg.
Register
File
Operand
MUX
ALU
Data Mem.
WB MUX
Instruction and control fields move through pipeline registers.
Arrows represent simplified data flow, not every wire.

## Slide 17
HOW ONE INSTRUCTION MOVES THROUGH THE PIPELINE
SCHEMATIC
15
IF
Fetch instruction
using PC
ID
Decode opcode
read registers
EX
ALU / memory /
write-back
Pipeline registers separate the stages and hold data/control values at clock edges.
• IF: PC selects the instruction address and instruction memory outputs the instruction.
• ID: opcode is decoded; source register values and immediate fields are prepared.
• EX: ALU executes the operation; memory and register write-back paths are used when needed.

## Slide 18
BRANCH / JUMP CONTROL AND FLUSH
SCHEMATIC
16
Branch / jump
instruction
Branch Unit
pc_sel
flush
PC MUX
• The Branch Unit evaluates jump/conditional-jump control using instruction flags.
• pc_sel tells the PC MUX whether to use the sequential address or jump target.
• flush clears younger pipeline instructions after a taken jump to reduce wrong-path execution.
• The supplied project material describes the jump decision as occurring in the EX stage.

## Slide 19
TESTBENCH: WHAT IS BEING CHECKED?
TESTBENCH
17
• A testbench is a separate Verilog module that drives clock/reset and checks outputs.
• tb_cpu instantiates cpu_top and observes PC, instruction, ALU result, write-back data, and flags.
• The testbench prints TIME lines to show sampled signal values.
• PASS means a check matched the expected value; FAIL means it did not.
• The current run reports 33 checks and 5 failures.
Clock (clk)
Reset (rst)
DUT: cpu_top
Assertions / checks

## Slide 20
BEHAVIORAL SIMULATION WAVEFORM
TESTBENCH
22
Signals shown in the Vivado/XSim waveform include clk, rst, checks, errors, PC, instruction, ALU output, write-back data, and flags.
clk
rst
PC
0
1
2
3
4
5
6
7
5
INSTR
c00
c00
645
683
060
6ca
470
a05
c00
ALU
0
0
5
3
8
a
2
0
0
WB
0
0
5
3
8
a
2
0
0
Waveform helps confirm signal timing, but the testbench's expected-versus-actual checks are needed to judge correctness.

## Slide 21
CURRENT VERIFICATION SUMMARY
TESTBENCH
23
33
checks
28
passed
5
failed
Failures visible in the log
• PC after reset: observed 0010, expected 0000.
• LDI R1: observed value does not match expected 0101.
• ADD R1 + R2: observed result does not match expected 1000.
• PC reset value and PC increment checks also fail.
The exact root cause cannot be confirmed from the log alone; inspect program_counter.v, reset polarity/timing, and the testbench sampling edges.

## Slide 22
RECOMMENDED DEBUGGING SEQUENCE
TESTBENCH
24
1
Check reset polarity
Confirm whether rst is active-high or active-low in program_counter.v and tb_cpu.v.
2
Check reset duration
Hold reset for enough clock edges, then release it away from the active sampling edge.
3
Inspect PC waveform
Compare clk, rst, pc_out at each rising edge; expected reset value should be unambiguous.
4
Trace instruction timing
Account for IF/ID and ID/EX latency before checking register write-back.
5
Re-run one test at a time
Start with PC reset/increment, then LDI, then ADD, then jump/flush.
These are debugging recommendations based on the displayed failures, not a claim that the cause is already known.

## Slide 23
CONCLUSION
WRAP-UP
25
• The design combines a 4-bit datapath with a 12-bit instruction format.
• The main blocks work together through the IF, ID, and EX stages.
• The schematic explains the data path, while the testbench checks behavior over time.
• The current simulation passes many checks but still has 5 failures out of 33.
• The next step is to fix PC reset/update behavior and re-verify LDI and ADD.
Design
Simulate
Debug → Verify
Thank you — Questions?